## Slide 1: Adaptive Weighted Traffic Splitting in Programmable Data planes
Kuo-Feng Hsu*, Praveen Tammana+, Ryan Beckett#, Ang Chen*, Jennifer Rexford+, David Walker+
Rice University*, Princeton University+, Microsoft Research#
Notes: Hello everyone, in this talk I am going to describe a novel data structure for load-aware traffic splitting in programmable data planes.

## Slide 2: Multiple paths between source-destination pairs
Datacenter networks
Capacity: 20.4Tbps
16 rack switches*
Switch chip:
32X40G
Private WANs
E.g: B4, SWAN
33 datacenter sites* and growing..
*src: B4andAfter [SIGCOMM’18].
Efficient load balancing is crucial to achieve good performance
Notes: To meet performance demand of modern applications, network operators typically provisions high bandwidth by exploiting multiple paths in the network.
For example, the capacity across paths is used to serve traffic between tor switches in data center networks and between data center sites in private wide area networks.
To achieve good performance, we need an efficient load balancing strategy.

## Slide 3: Motivation: Load-aware traffic splitting
Fast adaptation to real-time traffic conditions at RTT timescales
dest
load = 0
Equal split is desired
load > 0
Unequal split is desired
src1
src2
Traffic flows
dest
src1
src2
Notes: In particular, traffic splitting should quickly adapt to traffic conditions such as link failures or bursty workloads.
Take this network topology for example, …
No traffic from src2 => splitting traffic from src1 equally so that we can efficiently use the available bandwidth.
Some traffic from src2 => splitting traffic from src1 unequally is desired.
Notice that the workload is dynamic, the traffic condition can change very fast.
So the traffic splitting decisions should not only adapt to traffic condition but also adapt to it quickly.

## Slide 4: Existing approaches
Operates entirely in data plane
Control plane + Data plane
E.g.: HULA [SOSR’16], CONGA [SIGCOMM’14]
E.g.: HALO [ToN’15], TeXCP [SIGCOMM’05]
dest
src1
Best path
Probes
dest
src1
Probes
Traffic flows
Overloads the best path when RTTs are large
Unclear how these solutions can be realized using commodity data planes
Notes: Let’s see some existing approaches.
There are two classes of load-aware traffic splitting solutions:
In one class of solutions, all decisions are made entirely in data plane, such as Hula and Conga.
Take HULA for example, it periodically sends probes …
However, this may overload the best path especially when RTT is large.
Another line of works split traffic over multiple paths instead of a single path.
They also collect traffic conditions using mechanisms like probes,
But they assign path weights so that more traffic can go through paths with less congestion.
However, even though these solutions can split traffic across multiple paths at the same time, a control plane solution is too slow to adapt network conditions and it is unclear how they can work in today’s commodity data planes

## Slide 5: In this work..
Question
  How to balance load dynamically across
  multiple paths in the data plane?
Contributions
  We design new data structures for load-aware traffic splitting
  We characterize and study tradeoffs of these data structures
  We propose a data structure called DASH
Data
structure
Notes: In this work, we bridge the gap between these two classes of solutions
by addressing the question of how to balance the load across multiple paths entirely in the data plane.
So, we propose new data structures…

## Slide 6: Key problems
  (1) Spreading flows using a Path-to-Weight data structure
Data structure
Weights (1:3)
Traffic flows
Probe
  (2) Updating that data structure
  as probes arrive
Weights (1:3 )
Data structure
2:2
Notes: There are mainly two key functionalities that a traffic splitting data structure must support:
First, when the packets ….
Second, when the probes …

## Slide 7: PISA: Protocol Independent Switch Architecture
Programmable
Parser
Match + Action pipeline stages
Per-stage registers
Notes: Fortunately, the emerging programmable switches like p4 switches allow us to implement such data structures in data plane.
In P4 pipeline, There are several match+action stages, and each stage has its own registers.
We can design each stage to process the packets as we want.
The packet goes through a set of math-action tables spread across multiple stages.

## Slide 8: But, a constrained computational model
Limited #per-packet
register accesses
2. No access to registers mapped to a different stage
3. Small #stages and limited computation in each stage
Packet
Packet
Notes: However, there are some constraints.
First, When the packet arrives at one stage, it can only access…
Second, When the packet moves on to the next stage, it cannot access the registers in previous stages or any other stages …
Finally, because of the hardware limitation, the algorithm on the switch cannot be too complicated.

## Slide 9: Existing technique: Weighted Cost Multipathing (WCMP)
Replicates table entries with same pathID in proportion to its weight
A
C
B
C
C
B
Weight vector
1 : 2 : 3
Packet
header
Hash value
Paths: A, B, and C
WCMP table is
stored in a stage registers
Hash
How can we update
the table as probes arrive?
Notes: Now, we know the constraints, next I will show you some strawman solutions and how they violate those constraints.
To understand the strawman solutions, first we need to know one existing technique for weighted traffic splitting, WCMP.
The idea is to replicate table entries with the same path id so that number of entries for each path is in proportion to its weight.
With this table, we can spread the packets across multiple path as desired.
However, updating the WCMP table as probes arrive in a short time is challenging.
For example, assume we have three paths A, B, and C with weights … We may have a table like this.
Then, when a packet arrives, switch computes a hash value from the packet header fields, and uses the hash value as an index to get path id from the table.
However, updating the WCMP table as probes arrive on small time scales is challenging.

## Slide 10: Updating WCMP table
A
C
B
C
C
B
Requires many per-packet accesses to a stage registers
Current vector
1 : 2 : 3
Desired vector
3 : 2 : 1
Iterate over the table
A
A
A
B
B
C
Notes: One idea is to iterate over the table,
and for each path, we allocate corresponding number of entries in proportion to the desired weight.
But, in order to update every entry in the table, we need many accesses to the registers.
Given the aforementioned constraint, it is very difficult (if not impossible) to do this with one single probe packet,
especially when the table size is large.

## Slide 11: Updating WCMP table
Requires read and write to same register from different stages
Assign entries of non-deficit paths to deficit paths
Path | Count
A | 1
B | 2
C | 3
A
C
B
C
C
B
Before
Count
2
2
2
A
A
B
C
C
B
Count
3
2
1
A
A
B
A
C
B
Final result
Desired vector
A | 3
B | 2
C | 1
After packet 1
After packet 2
Notes: Another alternative is to divide the required updates to the table across multiple packets.
In our paper, we show a way to keep track of the number entries for paths so we can update the table more accurately.
I won’t cover the details, but notice to support this, we need to sequentially read multiple registers across multiple stages, and then write to the earlier registers again in a later stage.
Since the read-write to the same register from different stages cannot be supported, it would require packet recirculation. Therefore it is inefficient.

## Slide 12: DASH: Data-plane Adaptive Splitting with Hash threshold
A
B
C
Weight vector
1 : 2 : 3
H < 1
Stage 1
Check packet’s hash value against boundaries
H < 3
Stage 2
H < 6
Stage 3
Replicate pathID in WCMP table
Idea: Partition hash space into unique regions of size proportion to path weights
Packet
header
H = Hash
value
Hash
0 1 3 6
Boundaries are stored in per-stage registers
Notes: Finally, our proposal DASH works very differently from WCMP-based algorithms.
Instead of replicating table entries, DASH partitions the hash space into unique regions and assign one region to each path.
For example, assume we have three paths and their corresponding weights.
The hash space is divided into three regions, where the region size is in proportion to path weights.
And DASH will only store the boundaries between these regions in the registers,
So, when a packet arrives, DASH is able to determine the region the hash value matches and therefore the corresponding path the packet should be forwarded to.
So, when a packet arrives, DASH will generate the hash value based on the packet header fields and compare it against the boundaries of all regions so that we can determines the region the hash value matches and therefore the corresponding path the packet should be forwarded to.

## Slide 13: Updating DASH boundaries is simple
Desired vector = 3 : 2 : 1
New path boundary = Previous path’s boundary + Path region size
3+2=5
Stage 2
Probe
0+3=3
Stage 1
5+1=6
Stage 3
C
B
A
0 0+3=3
One per-packet access to stage registers
Read-write in the same stage
3+2=5
5+1=6
Used per-stage SALUs to execute addition operation
Fast and efficient
Notes: Updating boundaries in DASH is relatively simple compared to that in WCMP-based algorithms.
All we have to do is to calculate the boundaries by accumulating the weights one stage after the other.
For example, we have three paths with weights 3 2 and 1.
DASH will calculate the first boundary by adding the first weight ‘3’ to ‘0’, and calculate the second boundary by adding the second weight ‘2’ to the first boundary ‘3’, and we can get the third boundary in a similar way.
All these can be done during the process of the probe packet.
Because We only need to access one register per stage.
And, we do read and write to the same register in the same stage.
DASH is both fast and efficient.

## Slide 14: Evaluation
Prototype: Bmv2
Environment: Ns3
Workload:
  Web search [Alizadeh-SIGCOMM’15]
Schemes
  CP (Control plane): slow adaptation
  Hula: fast but single best path
  ECMP: traffic splitting but no adaptation
  DASH: traffic splitting and fast adaptation
Symmetric Fattree
10
30
50
70
90
2
4
8
FCT (sec)
Network load (%)
CP
Hula
ECMP
DASH
Notes: We built a prototype of DASH in ns3 simulation.
In this talk I will show you one set of experiment, you can find more interesting comparisons in our paper.
We used symmetric fattree, and ran different network load.
We measure flow competition time as performance metric, so lower is better.
We have three baselines,
First, control plane solution, it can only adapt to traffic condition slowly.
Second, it’s Hula, which can adapt to traffic condition but will only use one path at any given time.
Third, it’s ECMP, which can do traffic splitting across multiple paths at the same time, but it cannot adapt to traffic condition.
Our solution DASH, can do traffic splitting and fast adaptation. Therefore, it can outperform other solutions.

## Slide 15: Summary and future work
Adaptive weighted traffic splitting in the data plane
DASH is fast and efficient
Future work:
  Implementation in commodity switches (e.g., P4-Tofino)
  Building a distributed online traffic engineering system
Notes: In conclusion, we propose a data structure which enables adaptive weighted traffic splitting entirely in data plane.
This data structure, DASH, is fast and efficient compared to other strawman solutions.
As future work, We will implement DASH in commodity switches to show its feasibility.
And build a distributed traffic engineering system by integrating DASH with other weight updating algorithms in data plane to address the traffic dynamics in modern networks.
I concludes this talk with this slide and Thank you for your attention.

## Slide 16: Thank you

## Slide 17: Traffic splitting schemes (today)
Using traditional switches
  ECMP or WCMP with static path weights
  Cannot adapt quickly to dynamic traffic conditions
Using P4 based switches
  Enables a new range of possible solutions for fast adaptation
  E.g: HULA [SOSR’16]
Notes: However, this load-aware traffic splitting is not supported by traditional switches.
ECMP sets static path weights
So, it cannot …
Fortunately, the emerging programmable switches like P4 allows us to support fast adaptaion and one example is Hula.

## Slide 18: Contra tradeoffs
Contra chooses 1 best path and updates the best path as probes arrive
If probe frequency > new flows arrival rate
then
Contra gives new flows the best routes
If probe frequency << new flows arrival rate
then
Multiple new flows take the same path and overload the path
DC: Small RTTs and high probe frequency
Contra
WAN: Large RTTs and low probe frequency
Contra

## Slide 19: Current research
How to extend Contra to the multi-path WAN case?

## Slide 20: Why in the data plane?
Use case: Performance-aware distributed load balancing
  Quickly adapts to real-time network conditions
  E.g.: load spikes, failures
Process probes and update path weights
2: 2 1:3
Probe
Probe
Probe
Packet to path
assignment as per weights (1:3)
Data
Data
Data
Time to react can be kept close to the probe propagation time

## Slide 21: Updating Weighted Cost Multipath Table
Simple, but slow because update time is non-deterministic
Approach 2: Assign entries with probability
proportional to the desired vector
Desired vector
A | 3
B | 2
C | 1
Packet
1. Pick a path (say A)
A
B
B
C
C
C
2. Pick an entry
A
B
B
C
A
C
3. Update with
probability = 2/6
Before
After

## Slide 22: Updating Weighted Cost Multipath Table
Requires update to stateful memory at the end of the pipeline
Implementable in P4 with packet recirculation, but not efficient
Approach 2: Assign entries of non-deficit paths to deficit paths
Path | Count
A | 1
B | 2
C | 3
A
C
B
C
C
B
Before
Count
2
2
2
A
A
B
C
C
B
Count
3
2
1
A
A
B
A
C
B
After
Desired vector
A | 3
B | 2
C | 1

## Slide 23: Key Problems
  Maintaining the Path-to-Weight data structure as probes arrive
  Splitting traffic using that data structure
1. Split based on weights
Data structure
Weights (2:2)
Path A
Path B
Data
2. Update weights over time
Data structure
Weights (2:2 1:3)
Path A
Path B
Data

## Slide 24: Why in the data plane?
Probe
Probe
Probe
Time to react can be kept close to the probe propagation time
Packet or flow to path
assignment as per weights
Data structure
Weights (2:2)
Path A
Path B
Data
Probe processing and weight updates
in the order of RTTs
Goal: From (sec, minutes) to (usec, msec)
Weights (2:2 1:3)
Data structure

## Slide 25: Weighted traffic splitting
Spreads traffic across multiple non-equal components
  E.g.: Links, paths, and back-end servers

## Slide 26: Updating HashThreshold
A
0 B = 3
A
B
C
Current vector:
0 1 3 6
WA = 1 WB = 2 WC = 3
A
B
0 3 B +=WB=5
A
B
C
0 3 5 B+=WC=6
Desired vector:
WA = 3 WB = 2 WC = 1
Implementable in P4 and fast O(1)

## Slide 27: Goal: Weighted traffic splitting
1. Split based on weights
Data structure
Weights (2:2)
Path A
Path B
Data structure
Weights at time t2
2: 2 1:3
2. Update weights over time
Path A
Path B
Use case: Performance-aware distributed load balancing
  Quickly adapts to real-time network conditions
  E.g.: load spikes, failures
Data
Data
Data

## Slide 28: Motivation: Load-aware traffic splitting
Fast adaptation to real-time traffic conditions
(e.g: failures, traffic bursts)
50
50
0
100
80
20
30
100
30
B
Dest
A
B
Dest
A

## Slide 29: Motivation: Load-aware traffic splitting
Fast adaptation to real-time traffic conditions
(e.g: failures, congestion)
X

## Slide 30: Motivation: Load-aware traffic splitting
Dynamic
load balancing
P4 switches
Traffic
50
50
50
50
0
30
20
Traffic

## Slide 31: Routing goals
S
D
Traffic engineering (e.g.: min latency, max throughput)
Routing constraints (e.g.: Service chaining)
Fast adaptation (e.g.: failures, load changes)
Traffic flows
To extract maximum utility from one’s network one must optimize for..

## Slide 32: Contra [NSDI 2020]
A Programmable system for specifying and implementing
online optimization criteria
Contra program
Contra compiler
Performance-aware
routing
Probe generation
S
D
Probes
Probes
Best path
Traffic flows
Generates switch-level P4 programs
Switches process probes carrying network feedback and update best route