## Slide 1: Lessons Learned from the 9/11 Attacks
Jennifer Rexford
Princeton University
Thanks to Craig Partridge for slides from an earlier briefing…

## Slide 2
The Internet Under Crisis Conditions:
Learning from September 11
Computer Science and Telecommunications Board
The National Academies
Public release: Nov 2002
Study committee: Craig Partridge (Chair), Paul Barford, David D. Clark, Sean Donelan, Vern Paxson, Jennifer Rexford, and Mary Vernon
CSTB staff: Jon Eisenberg, Marjory Blumenthal, David Padgham, and D.C. Drake

## Slide 3: A 9/11 Timeline

## Slide 4: Early Morning
Up until 8:46 fairly routine
  Some network upgrades during the night
  Traffic beginning to increase with the work day
8:46 AA 11 crashes into WTC1
9:02 UA 175 crashes into WTC2
  Internet news servers rapidly inundated
9:37 AA 77 crashes into the Pentagon
9:39 NYC without broadcast TV and radio

## Slide 5: Mid-Morning
10:05 World Trade Center 2 collapses
  Internet infrastructure in WTC2 destroyed
10:28 World Trade Center 1 collapses
  At least one trans-atlantic link fails
  Internet traffic loads and connectivity drop
11:00 NYC cell phone call demand peaks
11:00 Internet connectivity close to normal
11:39 www.cnn.com now handling demand

## Slide 6: Afternoon
1:16 Part of the national 1-800 telephone network fails
4:35 First major electrical outage in NYC
  Substation in WTC 7
  Internet connectivity dips 2%
5:20 WTC 7 collapses
  Extensive damage to Verizon facility
  Internet connectivity dips 1%

## Slide 7: Evening
Three remaining data-comm centers in lower Manhattan struggle to keep operations running
  Dust causes air conditioning problems
  Operator error turns off generator at one facility
  Access limited
Restoration of service in NYC underway
Feeding network operators difficult
Operational issues continue several days

## Slide 8: Report Findings

## Slide 9: Findings
The Internet was mostly fine
  Little effect on Internet services as a whole
  Network displayed considerable flexibility
Limited measurements hamper analysis
  Limited data, and limited archiving of data
  Lack of a good “typical day” for baseline
Major effect on some Internet services
  2500% growth in demand for CNN site
  1300% growth in cell phone demand (11am)

## Slide 10: Findings
Use of Internet services was not typical
  Television and phone were primary services
  Internet servers as a backup for TV (news Web sites) and phone (instant messaging, VoIP)
  Understanding and enhancing the news
Inadequate redundancy in some parts
  ISPs concentrating facilities in one location
  Certain physical attacks could be worse
  Electronic attacks a more serious concern

## Slide 11: Findings
Subtle operational issues merit attention
  Network operators’ reliance on 1-800 numbers
  Internet and PSTN sharing fibers and conduits
  Planning for staff needing to eat and sleep
  Multi-day power outages, fuel deliveries, etc.
Better leveraging of Internet in the future
  Disaster plans should plan for Internet use
  Give some connectivity to all (IM, text msg)

## Slide 12: Anecdotes

## Slide 13: Anecdotes
CNN Web site
  The “one-packet homepage”
  Repurposing Turner server machines
  Re-Akamaizing the CNN Web site
Hidden dependencies
  South Africa top-level domain name server
  Authentication server for Florida ISP
  Intra-hospital network relying on the Internet
Better Internet stability in some places
  Network operators went home…

## Slide 14: Conclusions
The Internet on 9/11
  The Internet was relatively reliable
  Though some services were badly affected
  And application usage dramatically shifted
Lessons learned
  Better, more systematic measurement
  Uncovering hidden dependencies
  Addressing operational concerns