## Slide 1: Role of Theoretical Research in Networking Systems Development and Beyond
Jennifer Rexford
Princeton University

## Slide 2: Toward Networks Worthy of Society’s Trust
Networks are critical infrastructure
  But, they really were not designed for this
Networks are multi-faceted
  Many interacting protocols and layers
  Complex applications and user behavior
  Competing institutions and malicious actors
Networks are resource constrained
  Bandwidth, computation, memory, spectrum, …
Networks are too important (and too hard) to design without theory!

## Slide 3: Making Theory Meet Practice
Modeling existing systems
Optimizing system parameters
Designing new systems

## Slide 4: Programmability Helps Theory Meet Practice!
Switch OS
switch
Controller
Switch OS
switch
NIC
NIC
vSwitch
NIC
NIC
vSwitch
top to bottom
end to end
Notes: Can finally put the functionality we want, where we want it! But, to make this vision a reality, we need t

## Slide 5: Enabler: Programmable Data Planes
Stages
Deparser
Parser
Memory
Registers
ALU
Match-
Action
Table
p4.org

## Slide 6: Challenges: Resource Limitations
Limited
depth
Limited
# bits
Limited
# rules
Limited # registers
and # of accesses
Limited ALU
operations
Stages
Deparser
Parser
Memory
Registers
ALU
Match-
Action
Table

## Slide 7: Efficient Data-Plane Data Structures
Approximate analysis is fine
  Microbursts: size estimate for just the large flows
  DDoS: rough count for large #s of distinct sources
  Path performance: rough estimates for best paths
Data structures can fit in data-plane registers
  Sketch (e.g., Bloom filter, count-min sketch, etc.)
  Small hash table (e.g., cache of the popular keys)
Notes: Collaboration with the theoretical computer science community (streaming algorithms, compact data structures)

## Slide 8: Deploying Data-Plane Data Structures
Programmable devices
  Barefoot Tofino switches
  FPGA-based network interface cards
Practical deployments
  Princeton University campus
  AT&T backbone trial deployment
  ONF Aether 5G platform (prontoproject.org)
Example use cases
  Microburst analytics
  Heavy hitter detection
  Round-trip time monitoring
Internet2
Tofino
Neuroscience
Institute
https://p4campus.cs.princeton.edu/

## Slide 9: Programming Language Abstractions
Switch OS
switch
Controller
Switch OS
switch
NIC
NIC
vSwitch
NIC
NIC
vSwitch
Compiler
Network-wide goals (objectives and constraints)
Per-device programs (measure, analyze, and control)

## Slide 10: Conclusion
Network systems need theoretical foundations
  So we can design networks worthy of society’s trust
Theory needs to meet practice
  So good ideas can see the light of day
Deep programmability enables theory to meet practice
  Putting the functionality we want, where we want it
Programmable networks also need a strong foundation
  Efficient data structures that run in the data plane
  Expressive programming abstractions and effective compilers

## Slide 11: Example References
Data-plane data structures
  Microbursts: https://www.cs.princeton.edu/~jrex/papers/conquest19.pdf
  Heavy hitters: https://www.cs.princeton.edu/~xiaoqic/documents/paper-PRECISION-ToN.pdf and https://www.cs.princeton.edu/~jrex/papers/carpe20.pdf
  Count distinct: https://www.cs.princeton.edu/~xiaoqic/documents/paper-BeauCoup-SIGCOMM20.pdf
  Performance: https://www.cs.princeton.edu/~jrex/papers/apocs20.pdf
Language abstractions
  Traffic queries: https://www.cs.princeton.edu/~jrex/papers/sonata.pdf
  Path queries: https://www.cs.princeton.edu/~jrex/papers/pathquery16.pdf
  Performance-aware routing: https://www.cs.princeton.edu/~jrex/papers/contra20.pdf