## Slide 1: Scalable Multi-Class Traffic Management in Data Center Backbone Networks
Amitabha Ghosh (UtopiaCompression)
Sangtae Ha (Princeton)
Edward Crabbe (Google)
Jennifer Rexford (Princeton)

## Slide 2: Outline
Motivation
Contributions
Model and Formulation
Scalable Designs
Performance Evaluation
Conclusions

## Slide 3: Motivations
Multiple interconnected data centers (DCs) with multiple paths between them
DCs, traffic sources, and backbone owned by the same OSP, e.g., Google, Yahoo, Microsoft
Backbone
Traffic with different performance requirements
Different business importance
Data center & host

## Slide 4: Contributions
Controlling the three “knobs”
  Sending rates of hosts
  Weights on link schedulers
  Splitting of traffic across paths
Joint optimization of rate control, routing, and link scheduling
Data center backbone
Source DC & host
Destination host & DC
Edge router

## Slide 5: Contributions
Computation is distributed across multiple tiers using a few controllers
Result is provably optimal using optimization decomposition
Semi-centralized solutions viable and, in fact, preferred in practice, e.g., Google’s B4 globally-deployed software defined private WAN (SIGCOMM ‘13)
Fully-centralized
Not scalable
Fully-distributed
Scaling issues due to message passing, slow convergence
Semi-centralized: Our work
Modular, scalable with low message-passing and fast convergence
TRUMP (CoNEXT ‘07)
DaVinci (CoNEXT ‘08)

## Slide 6: Model and Formulation
Traffic Model
  Performance requirements Set of traffic classes
  Multiple flows per class
    Flow: traffic between a source-destination pair
  Business importance flow weight
Utility Function of a Class
  All flows in the same class have the same utility function
  For simplicity, assume only throughput and delay sensitive traffic

## Slide 7: Model and Formulation
Network Model
  Set of unidirectional links
    Capacity
    Propagation delay
  Set of paths
  Routing matrix
  One queue per class
  Multi-path routing
    Path rate of flow s of class k over path p
Topology matrix
Path routing matrix
smaller
larger

## Slide 8: Model and Formulation
Throughput sensitivity of class k, e.g., log(.)
Delay sensitivity of class k
Weight of flow s of class k
Coefficients to model different degrees of sensitivity to throughput and delay
Total sending rate of flow s of class k
Utilization of class k over link l
Utility of Flow s of Class k
Sum of the products of path rates and average end-to-end delays on those paths

## Slide 9: Model and Formulation
Objective Function
  Data centers, backbone and traffic sources under the same OSP ownership
  Maximize the sum of utilities of all flows across all traffic classes (global “social welfare”)
Global Problem G:

## Slide 10: Two-Tier Design
Network
C1
CK
Classes
. . .
F
F
F
F
F
F
F
Flows
Link Coordinator (LC)
Optimizes aggregate link bandwidth across classes
Class Allocator (CA)
Optimizes sending rates across flows in its own class
A centralized entity
Knows network topology
One for each class
Knows the utility function, weights, and paths of individual flows in its own class
Each controller has a limited view about the network and inter-DC traffic
Coordination

## Slide 11: Two-Tier Design
Network
C1
CK
Classes
. . .
F
F
F
F
F
F
F
Flows
Message-passing
Message-passing
Coordination

## Slide 12: Two-Tier Decomposition
Primal Decomposition
Link Coordinator
Coordinates all the subproblems
Class Allocator
Solves independently

## Slide 13: Two-Tier Decomposition
Primal Decomposition
Link Coordinator
Coordinates all the subproblems
Class Allocator
Solves independently
Subproblem for Class k

## Slide 14: Two-Tier Decomposition
Primal Decomposition
Link Coordinator
Coordinates all the subproblems
Class Allocator
Solves independently
Subproblem for Class k
Master Primal

## Slide 15: Two-Tier Decomposition
Primal Decomposition
Link Coordinator
Coordinates all the subproblems
Class Allocator
Solves independently
Message-Passing

## Slide 16: Three-Tier Design
Network
C1
CK
Classes
. . .
F
F
F
F
F
F
F
Flows
Why another tier? (High control overhead)
  Flow of a given class may originate from any DC
  Each class allocator potentially communicates with all DCs

## Slide 17: Three-Tier Design
Network
C1
CK
Classes
. . .
F
F
F
F
F
F
F
Flows
Why another tier? (High control overhead)
  Flow of a given class may originate from any DC
  Each class allocator potentially communicates with all DCs
C1
CK
Classes
. . .
DC1
DCj
DCJ
F
F
F
F
F
F
F
Flows
. . .
. . .
Data centers

## Slide 18: Three-Tier Design
Network
C1
CK
Classes
. . .
DC1
DCj
DCJ
F
F
F
F
F
F
F
Flows
. . .
. . .
Data centers
Link Coordinator (LC)
Optimizes aggregate link bandwidth across classes
Class Allocator (CA)
Optimizes aggregate link bandwidth across DCs sending traffic in its own class
Data Center Allocator (DCA)
Optimizes sending rates across flows in its own class originating from its own DC
One centralized entity
One per class
One per class, per DC

## Slide 19: Three-Tier Design
Message-passing
Message-passing
Message-passing

## Slide 20: Three-Tier Decomposition
2-Level Primal Decomposition
Link Coordinator
Coordinates the secondary primals
Class Allocator
Coordinates the subproblems of its own class
Data Center Allocator
Solves independently

## Slide 21: Three-Tier Decomposition
Message-Passing
Inner loop
faster
Outer loop
slower

## Slide 22: Performance Evaluation
4 DCs
1 Gbps link capacity in each direction
First 3 shortest possible paths between every pair of DCs (36 total)
Two classes with log utility functions
Abilene topology
Performance Metrics
  Rate of convergence
  Message-passing overhead
Simple topology
DC1 & DC2 send traffic to DC3
100 Mbps link capacity
Two classes with log utility

## Slide 23: Rate of Convergence
Each iteration is in the order of a few seconds:
  There can be only so many different types of performance requirements (~10)
  Only so many inter-connected DCs (a few 10s)
Two-tier
Three-tier

## Slide 24: Rate of Convergence
Three-tier: Number of iterations to converge for different combinations of class-level and DC-level step sizes.

## Slide 25: Rate of Convergence
Summary of the convergence behavior
In practice, choose step sizes that converge quickly.
Dynamic traffic demand: For private OSP backbone, the demand variability can be controlled to some extent

## Slide 26: Message-Passing Overhead
Two-tier:
# of variables
Three-tier:
# of variables
No. of classes
No. of backbone links
No. of DCs
No. of class-level allocations to converge in two-tier and three-tier designs
No. of DC-level allocations to converge in three-tier
(Until convergence)
Messages are sent over the wide area network
Number of messages depends on the number of flows in the two-tier design, but not in the three-tier design
Small compared to the total traffic volume
100
5

## Slide 27: Conclusions
Software defined traffic management for wide area data center backbone networks
Two scalable and practical semi-centralized designs using a small number of controllers that can be implemented in real-world data center backbones (Google)
Joint rate control, routing, and link scheduling using optimization in a modular, tiered design
Results provably optimal using principles of optimization decomposition
Tradeoff between rate of convergence and message-passing – choose the design that suits the OSP best

## Slide 28: Thank You
Amitabha Ghosh, Sangtae Ha, Edward Crabbe, and Jennifer Rexford, “Scalable Multi-Class Traffic Management in Data Center Backbone Networks,” IEEE JSAC: Networking Challenges in Cloud Computing Systems and Applications, vol. 13, no. 12, 2013 (in press).
http://anrg.usc.edu/~amitabhg/papers/JSAC-CloudComputing-2013.pdf