## Slide 1: Programmable In-Network Obfuscation of DNS Traffic
Liang Wang, Hyojoon Kim, Prateek Mittal, Jennifer Rexford
Princeton University

## Slide 2
Do53 Traffic Reveals Sensitive Information
Client at [1.2.3.4] will visit website [X]
Client A
(IP = 1.2.3.4)
Public DNS resolver
Query: Domain X
Network-level adversary

## Slide 3
Even Encrypted DNS Communications Reveal Sensitive Information
Client A
(IP = 1.2.3.4)
Public DNS resolver
Query: Domain X
DNSCrypt, DNS-over-TLS, DNS-over-HTTPS,...
Client at [1.2.3.4] will visit website [???]
Network-level adversary

## Slide 4
Encrypted DNS: DNS Resolver --- A Single Point of Privacy Failure
Client A
(IP = 1.2.3.4)
Public DNS resolver
Query: Domain X
Client at [1.2.3.4] will
visit website [X]
Need to hide client IP addresses from DNS resolvers
DNSCrypt, DNS-over-TLS, DNS-over-HTTPS,...
Client at [1.2.3.4] will visit website [???]
Curious server
Network-level adversary

## Slide 5
Proxy-based DNS Protects Client IP Addresses
Client A
(IP = 1.2.3.4)
Public DNS resolver
Query: Domain X
srcIP = 1.2.3.4
Query: Domain X
Proxy
(IP = 2.3.4.5)
srcIP = 2.3.4.5
Solutions: DNS over Tor, Anonymized DNSCrypt, Oblivious DNS, Oblivious DoH, …
Client at [1.2.3.4] will visit [???]
Client at [???] will
visit website [X]
Curious server
Network-level adversary

## Slide 6
Proxy-based DNS: Practical Challenges
Solutions: DNS over Tor, Anonymized DNSCrypt, Oblivious DNS, Oblivious DoH, …
Higher latency
Modifications to DNS client / infrastructure
Need a lightweight IP anonymization method that requires no modifications to DNS client and server
High deployment barriers for proxy-based solutions

## Slide 7
Can We Embed Proxy in Network Elements?
Programmable data-plane hardware
  Offload privacy functionality to the network
    High speed
    Avoid end user involvement
Growing ubiquity of IPv6 in the Internet core
  Use IPv6 address to embed information
Opportunities:

## Slide 8
Our Solution: PINOT
PINOT: A lightweight in-network IP address obfuscation system
Goal: Prevent public DNS services from associating client IP addresses to queries
Use programmable switch to encrypt IP addresses at a high speed (12.8 Tbps)
No modification to DNS protocols; No additional client software installation
Complementary to encrypted DNS

## Slide 9
PINOT in An Edge Network
IPv4 Edge network
Public DNS resolver
Client A
(IP = 1.2.3.4)
PINOT switch
Query: Domain X
Do53
DNSCrypt
Query: Domain X
srcIP =[Encrypted IP]
srcIP =[Encryped IP]
Client at [???] will
visit website [X]
Run PINOT at the network border
  DNS requests: Encrypt the source IP address in each packet
Assumption: A DNS request can fit into a single packet

## Slide 10
PINOT in An Edge Network
Public DNS resolver
Client A
(IP = 1.2.3.4)
PINOT switch
Response
dstIP=1.2.3.4
Client at [???] will
visit website [X]
Run PINOT at the network border
  DNS requests: Encrypt the source IP address in each packet
  DNS responses: Decrypt the destination IP address and forward packets
Response
dstIP =[Encrypted IP]
IPv4 Edge network

## Slide 11
Challenges
Perform encryption on resource-constrained programmable switch
Receive return traffic without cooperation
Work with asymmetric routing

## Slide 12
Programmable Switch Resource Constraints
Limited memory
Limited operations
    1 pipeline: a small number of stages
    1 stage: a limited number of table lookups, and math/logical ops
Packet
…
Processed
packet
Packet processing pipeline
Stage

## Slide 13
Efficient Encryption of IP in Data Plane
Solution: Two-round Even-Mansour encryption (2EM)
AES is too expensive on data plane
XOR
XOR
XOR
Permutation
(S-Box + Straight P-box)
Permutation
Plaintext
Ciphertext
Key1
Key2
Key3
2EM can be implemented using table lookups and XORs

## Slide 14
Efficient Encryption of IP in Data Plane
  Encrypt IP using a single pass through packet processing pipeline
  Encrypt packets at 3.2 Tbps on our Intel Tofino switch!
  Pad IPv4 address with random bits for stronger security and privacy
  Consecutive requests from the same client have distinct client source IP addresses
Solution: Two-round Even-Mansour encryption (2EM)
AES is too expensive on data plane
See paper for more details

## Slide 15
IPv6 Encoding for Stateless Encryption and Routing
Challenge:
  Store ciphertext (> 32 bits) and encryption metadata (key version #)
  Ensure successful routing of return traffic
Solution: Convert IPv4 packets to IPv6 packets
  Information required for decryption are stored in IPv6 address
  PINOT only stores encryption keys
Client IPv4 address
Reserved IPv6 network prefix
Random padding
Ver#
+
->
Encrypted IPv4 address
Encrypted IPv4 address
New IPv6 address
PINOT is stateless

## Slide 16
IPv6 Encoding for Stateless Encryption and Routing
Solution: A centralized controller for distributing the per-AS secret keys
PINOT can handle asymmetric routing easily
Challenge: Return traffic can go to any ingress point
Controller

## Slide 17
PINOT is Complementary to Encrypted DNS
*Assuming an encrypted DNS solution has already been deployed, using PINOT to achieve IP obfuscation does not require modifying the existing DNS client/server software
Using PINOT with encrypted DNS protocols offers better privacy with little performance overhead
 | Query encryption | IP hiding | Modification to client | Proxy overhead
Do53 | No | No | - | -
Encrypted | Yes | No | Yes | -
Proxy | Yes | Yes | Yes | High
PINOT + Do53 | No | Yes | No | Low
PINOT + Encrypted | Yes | Yes | No* | Low

## Slide 18
18
Real-World Deployment of PINOT at Princeton
PINOT source Code: https://github.com/liangw89/p4privacy/tree/master/pinot
Wedge 100BF-32X
Tofino switch
2620:c4:0:fc::/64

## Slide 19
19
Evaluation of PINOT for Do53
Target resolver: 350+ public resolvers with both IPv4 and IPV6 support
Query: 10 queries for random domains from Top 1M to each resolver
Setting: IPv6 network, IPv4 network, and IPv4 + PINOT
PINOT is feasible
  DNS responses are consistent across settings
PINOT introduces low latency
  Potential overhead: IPv6 and IPv4 packets take different routing paths
  PINOT does not add extra latency in 97% of the cases

## Slide 20
PINOT for Other Connectionless Protocols
NTP: IPv6 host discovery and scanning
  Single-packet protocol like DNS
WireGuard VPN: Client IP address collection
  Crypto-key routing allows per-packet encryption without
    disrupting connectivity
PINOT prevents the public NTP/WireGuard VPN servers from learning the real client IP addresses

## Slide 21
Conclusion
PINOT, an in-network proxy service
Low performance overhead
Low deployment barriers
  Single network
  No modification to DNS
  No cooperation from end-users
A network deploy can PINOT to provide extra privacy for users as a
value-added service
A useful building block for bootstrapping more privacy applications!

## Slide 23
PINOT Variants
PINOT for IPv6 network
  Use the lowest 64 bits of IPv6 address for encryption
PINOT for connection-oriented protocols
  Need to maintain per-connection state
  Work with DoH and DoT