## Slide 1: SDX: A Software-Defined Internet eXchange
Jennifer Rexford
Princeton University
http://sdx.cs.princeton.edu

## Slide 2: Software Defined Networking
Changing how we design and manage networks
  Data centers, backbones, enterprises, …
But, so far, mostly inside these networks
  Network virtualization, traffic engineering, …
In this talk:
  Fundamentally change interdomain traffic delivery
  Starting with SDN at boundaries between domains

## Slide 3: Wide-Area Traffic Delivery
1
2
3
4
5
6
7
~50,000 Autonomous Systems (ASes)
Notes: Wide-area traffic delivery happens through the cooperation (and competition) of 50K or so separately administered networks.

## Slide 4: Border Gateway Protocol (BGP)
Interdomain routing on IP address blocks
1
2
3
4
5
6
7
12.34.56.0/24
Web server
Notes: They coordinate by propagating information about how to reach blocks of IP addresses, or IP prefixes, using the Border Gateway Protocol.
But BGP was designed for a different era.

## Slide 5: BGP is Not Flexible Enough
Routing only on destination IP address blocks
  (No customization of routes by application or sender)
Can only influence immediate neighbors
  (No ability to affect path selection remotely)
Indirect control over packet forwarding (Indirect mechanisms to influence path selection)
Enables only basic packet forwarding (Difficult to introduce new in-network services)

## Slide 6: Valuable Wide-Area Services
Application-specific peering
  Route video traffic one way, and non-video another
Blocking denial-of-service traffic
  Dropping unwanted traffic further upstream
Server load balancing
  Directing client requests to different data centers
Steering through network functions
  Transcoders, scrubbers, caches, crypto, …
Inbound traffic engineering
  Splitting incoming traffic over multiple peering links

## Slide 7: Enter Software-Defined Networking
Match packets on multiple header fields (not just destination IP address)
Control entire networks with a single program (not just immediate neighbors)
Direct control over packet handling (not indirect control via routing protocol arcana)
Perform many different actions on packets (beyond basic packet forwarding)

## Slide 8: Deploy SDN at Internet Exchanges
Leverage: SDN deployment even at single IXP can benefit tens to hundreds of providers
  Without providers deploying new equipment!
Innovation hotbed: Incentives to innovate, as IXPs on front line of peering disputes
Growing in numbers:
  350-400 IXPs
  ~100 new IXPs established in past few years
Notes: Content delivery
Keep local traffic local (cost, performance, privacy/wiretapping)

## Slide 9: SDX: Software-Defined eXchange (SIGCOMM’14 paper)
Arpit Gupta, Nick Feamster, Laurent Vanbever, Muhammad Shahbaz, Sean Donovan, Brandon Schlinker, Scott Shenker, Russ Clark, Ethan Katz-Bassett
Princeton University, Georgia Tech, UC Berkeley, USC
http://sdx.cs.princeton.edu

## Slide 10: Conventional IXPs
AS A Router
AS C Router
AS B Router
BGP Session
Switching Fabric
IXP
Route Server
Notes: So let’s first take a look as what a typical Exchange Point looks like.
Exchange points have multiple participants. Their edge routers are connected to each other using using IXP’s switching fabric.
These edge routers use the IXP’s route server to exchange BGP routes with each other.

## Slide 11: SDX = SDN + IXP
AS A Router
AS C Router
AS B Router
BGP Session
SDN Switch
SDX Controller
SDX
Notes: Compared to these IXPs, we replace the switching fabric with SDN switches and the route server with SDX controller.
This SDX controller,
subsumes router server’s behavior of exchanging BGP routes
It also takes participant’s SDN specific policies as input, combines them together and pushes down the set of OF rules.

## Slide 12: Prevent DDoS Attacks
AS 2
AS 1
AS 3
SDX 1
SDX 2
Notes: A participant doesn’t need to be physically at the exchange

## Slide 13: Prevent DDoS Attacks
AS 2
AS 1
AS 3
SDX 1
SDX 2
Attacker
Victim
AS1 under attack originating from AS3

## Slide 14: Use Case: Prevent DDoS Attacks
AS 2
AS 1
AS 3
SDX 1
SDX 2
Attacker
Victim
AS1 can remotely block attack traffic at SDX(es)

## Slide 15: SDX-based DDoS protection vs. Traditional Defenses/Blackholing
Remote influence
  Physical connectivity to SDX not required
More specific
  Drop rules based on multiple header fields, source address, destination address, port number …
Coordinated
  Drop rules can be coordinated across multiple IXPs
Notes: There are bunch of other applications that are also possible with SDX and you find more details about them in the paper.

## Slide 16: Inbound Traffic Engineering
AS A Router
AS C Routers
AS B Router
SDX Controller
SDX
C1
C2
10.0.0.0/8
Notes: Now let’s consider another scenario where AS C’s policy is to receive HTTP traffic on C2.

## Slide 17
AS A Router
AS C Routers
AS B Router
C1
C2
Incoming Data
Inbound Traffic Engineering
10.0.0.0/8
Incoming Traffic | Out Port | Using BGP | Using SDX
dstport = 80 | C1 |  | 
Notes: Now let’s consider another scenario where AS C’s policy is to receive HTTP traffic on C2.
Now such a fine grained policy is not possible with BGP

## Slide 18
AS A Router
AS C Routers
AS B Router
C1
C2
Incoming Data
Inbound Traffic Engineering
10.0.0.0/8
Incoming Traffic | Out Port | Using BGP | Using SDX
dstport = 80 | C1 | ? | 
Fine grained policies not possible with BGP

## Slide 19
Incoming Traffic | Out Port | Using BGP | Using SDX
dstport = 80 | C1 | ? | match(dstport =80) fwd(C1)
AS A Router
AS C Routers
AS B Router
C1
C2
Incoming Data
Inbound Traffic Engineering
10.0.0.0/8
Enables fine-grained traffic engineering policies
Notes: So SDX enables more direct & fine grained traffic control which is not possible in current networks.
There are bunch of other applications that are also possible with SDX and you find more details about them in the paper.

## Slide 20: Building SDX is Challenging
Programming abstractions
  How networks define SDX policies and how are they combined together?
Interoperation with BGP
  How to provide flexibility w/o breaking global routing?
Scalability
  How to handle policies for hundreds of peers, half million address blocks, and matches on multiple header fields?
Notes: So far it looks like SDX is the solution which can enable more flexible peering arrangements, & more direct & flexible traffic control, but building a real deployable SDX is not easy.
The first challenge is to define the right programming abstractions, i.e how can participants express policies independently. Another challenge is that all the SDX participants share the same switching fabric, so their policies need to be combined together and translated into set of flow rules. So we also need to define the right abstractions for combining participant’s policies together.
Another challenge is the fact that we have SDN specific policies at the IXP and every one else is using BGP. So we have to make sure that participants’ policies safely interact with BGP, w/o creating any forwarding loops or blackholes.
And finally we are talking about thousands of prefixes, hundreds of peers and matches on multiple header fields, we need to take scalability into considerations

## Slide 21: Building SDX is Challenging
Programming abstractions
  How networks define SDX policies and how are they combined together?
Interoperation with BGP
  How to provide flexibility w/o breaking global routing?
Scalability
  How to handle policies for hundreds of peers, half million prefixes and matches on multiple header fields?

## Slide 22: Directly Program the SDX Switch
B1
A1
C1
C2
match(dstport=80)fwd(C1)
match(dstport=80)fwd(C)
Switching Fabric
AS A & C directly program the SDX Switch
Notes: All the participants share the same switching fabric. One option is that they can all directly express policies for this switch.

## Slide 23: Virtual Switch Abstraction
Each AS writes policies for its own virtual switch
AS A
C1
C2
B1
A1
AS C
AS B
match(dstport=80) fwd(C)
match(dstport=80)fwd(C1)
Virtual Switch
Virtual Switch
Virtual Switch
Switching Fabric
Notes: For that we came up with Virtual Switch Abstraction. Here each AS is provided with their own virtual SDX switch for which they express their policies.
These policies are applied only if traffic enters or leaves their network.

## Slide 24: Combining Participant’s Policies
Synthesize: match(inport=A1 & dstport=80)  fwd(C1)
AS A
C1
C2
B1
A1
AS C
AS B
match(dstport=80)fwd(C1)
Virtual Switch
Virtual Switch
Virtual Switch
Switching Fabric
p
match(dstport=80)fwd(C)
Notes: ….
This approach naturally resolves policy conflicts, as it follows packets to determine the order in which policies should be applied.

## Slide 25: Building SDX is Challenging
Programming abstractions
  How networks define SDX policies and how are they combined together?
Interoperation with BGP
  How to provide flexibility w/o breaking global routing?
Scalability
  How to handle policies for hundreds of peers, half million address blocks, and matches on multiple header fields?

## Slide 26: SDX Platform
Running code with full BGP integration
  Github available from http://sdx.cs.princeton.edu
SDX testbeds:
  Transit Portal for “in the wild” experiments
  Mininet for controller experiments
Exploring deployment opportunities
  Princeton, DOD/IC, GENI, SOX, Internet2, ESnet
  Regional IXPs in US, Europe, and Africa
Notes: So far we have developed a prototype of SDX. We have two different types of SDX testbeds. One uses Transit portal to bring live traffic to the SDX switch and the other uses virtual containers in Mininet to emulate edge routers. We also have a demo after this session which shows how we develop two applications using SDX and how they interoperate with each other.
You can find more details about this testbed from our github repo. We also have instructions for users to get started with SDX and try out their own new applications.

## Slide 27: Conclusion
The Internet is changing
  New challenges for content delivery
  Increasing importance of IXPs
SDN can let providers innovate
  New capabilities and abstractions
Next steps
  Operational deployments
  Additional SDX applications
  Distributed exchange points