## Slide 1: SDX: A Software-Defined Internet Exchange
Arpit Gupta
Laurent Vanbever, Muhammad Shahbaz, Sean Donovan,
Brandon Schlinker, Nick Feamster, Jennifer Rexford,
Scott Shenker, Russ Clark, Ethan Katz-Bassett
Georgia Tech, Princeton University, UC Berkeley, USC

## Slide 2: The Interdomain Ecosystem is Evolving ...
Flatter and densely interconnected Internet*

## Slide 3: …But BGP is Not
Routing only on destination IP prefixes
  (No customization of routes by application, sender)
Can only influence immediate neighbors
  (No ability to affect path selection remotely)
Indirect control over data-plane forwarding (Indirect mechanisms to influence path selection)
How to overcome BGP’s limitations?

## Slide 4: SDN for Interdomain Routing
Forwarding on multiple header fields (not just destination IP prefixes)
Ability to control entire networks with a single software program (not just immediate neighbors)
Direct control over data-plane forwarding (not indirect control via control-plane arcana)
How to incrementally deploy SDN for
Interdomain Routing?

## Slide 5: Deploy SDN at Internet Exchanges
Leverage: SDN deployment even at single IXP can yield benefits for tens to hundreds of ISPs
Innovation hotbed: Incentives to innovate as IXPs on front line of peering disputes
Growing in numbers: ~100 new IXPs established in past three years*

## Slide 6: Background: Conventional IXPs
AS A Router
AS C Router
AS B Router
BGP Session
Switching Fabric
IXP
Route Server

## Slide 7: SDX = SDN + IXP
AS A Router
AS C Router
AS B Router
BGP Session
SDN Switch
SDX Controller
SDX

## Slide 8: SDX Opens Up New Possibilities
More flexible business relationships
  Make peering decisions based on time of day, volume of traffic & nature of application
More direct & flexible traffic control
  Define fine-grained traffic engineering policies
Better security
  Prefer “more secure” routes
  Automatically blackhole attack traffic

## Slide 9: Use Case: Inbound Traffic Engineering
AS A Router
AS C Routers
AS B Router
SDX Controller
SDX
C1
C2
10.0.0.0/8

## Slide 10
AS A Router
AS C Routers
AS B Router
C1
C2
Incoming Data
Use Case: Inbound Traffic Engineering
10.0.0.0/8
Incoming Traffic | Out Port | Using BGP | Using SDX
dstport = 80 | C1 |  | 

## Slide 11
AS A Router
AS C Routers
AS B Router
C1
C2
Incoming Data
Use Case: Inbound Traffic Engineering
10.0.0.0/8
Incoming Traffic | Out Port | Using BGP | Using SDX
dstport = 80 | C1 | ? | 
Fine grained policies not possible with BGP

## Slide 12
Incoming Traffic | Out Port | Using BGP | Using SDX
dstport = 80 | C1 | ? | match(dstport =80) fwd(C1)
AS A Router
AS C Routers
AS B Router
C1
C2
Incoming Data
Use Case: Inbound Traffic Engineering
10.0.0.0/8
Enables fine-grained traffic engineering policies

## Slide 13: Building SDX is Challenging
Programming abstractions
  How networks define SDX policies and how are they combined together?
Interoperation with BGP
  How to provide flexibility w/o breaking global routing?
Scalability
  How to handle policies for hundreds of peers, half million prefixes and matches on multiple header fields?

## Slide 14: Building SDX is Challenging
Programming abstractions
  How networks define SDX policies and how are they combined together?
Interoperation with BGP
  How to provide flexibility w/o breaking global routing?
Scalability
  How to handle policies for hundreds of peers, half million prefixes and matches on multiple header fields?

## Slide 15: Directly Program the SDX Switch
B1
A1
C1
C2
match(dstport=80)fwd(C1)
match(dstport=80)drop
Switching Fabric
AS A & C directly program the SDX Switch

## Slide 16: Conflicting Policies
drop? C1?
B1
A1
C1
C2
Switching Fabric
How to restrict participant’s policy to traffic it sends or receives?
match(dstport=80)drop
match(dstport=80)fwd(C1)

## Slide 17: Virtual Switch Abstraction
Each AS writes policies for its own virtual switch
AS A
C1
C2
B1
A1
AS C
AS B
match(dstport=80)drop
match(dstport=80)fwd(C1)
Virtual Switch
Virtual Switch
Virtual Switch
Switching Fabric

## Slide 18: Combining Participant’s Policies
Policy(p) = PolA  PolC
AS A
C1
C2
B1
A1
AS C
AS B
match(dstport=80)fwd(C1)
Virtual Switch
Virtual Switch
Virtual Switch
Switching Fabric
p
match(dstport=80)fwd(C)
PolA
PolC

## Slide 19: Building SDX is Challenging
Programming abstractions
  How networks define SDX policies and how are they combined together?
Interoperation with BGP
  How to provide flexibility w/o breaking global routing?
Scalability
  How to handle policies for hundreds of peers, half million prefixes and matches on multiple header fields?

## Slide 20: Requirement: Forwarding Only Along BGP Advertised Routes
A
C
B
SDX
10/8
20/8
match(dstport=80)  fwd(C)

## Slide 21: Ensure ‘p’ is not forwarded to C
match(dstport=80)  fwd(C)
A
C
B
SDX
10/8
20/8
p
dstip = 20.0.0.1
dstport = 80

## Slide 22: Solution: Policy Augmentation
A
C
B
SDX
10/8
20/8
(match(dstport=80) && match(dstip = 10/8)) fwd(C)

## Slide 23: Building SDX is Challenging
Programming abstractions
  How networks define SDX policies and how are they combined together?
Interoperation with BGP
  How to provide flexibility w/o breaking global routing?
Scalability
  How to handle policies for hundreds of peers, half million prefixes and matches on multiple header fields?

## Slide 24: Scalability Challenges
Reducing Data-Plane State: Support for all forwarding rules in (limited) switch memory (millions of flow rules possible)
Reducing Control-Plane Computation: Faster policy compilation (policy compilation takes hours for initial compilation)

## Slide 25: Scalability Challenges
Reducing Data-Plane State: Support for all forwarding rules in (limited) switch memory millions of flow rules possible
Reducing Control-Plane Computation: Faster policy compilation policy compilation could take hours

## Slide 26: Reducing Data-Plane State: Observations
Internet routing policies defined for groups of prefixes.*
Edge routers can handle matches on hundreds of thousands of IP prefixes.

## Slide 27: Reducing Data-Plane State: Solution
10/8
40/8
20/8
Group prefixes with similar forwarding behavior
SDX Controller

## Slide 28: Reducing Data-Plane State: Solution
10/8
40/8
20/8
Advertise one BGP next hop for each such
prefix group
Edge router
forward to
BGP Next Hop

## Slide 29: Reducing Data-Plane State: Solution
fwd(1)
fwd(2)
forward to
BGP Next Hop
match on
BGP Next Hop
Flow rules at SDX match on BGP next hops
SDX FIB
10/8
40/8
20/8
Edge router

## Slide 30: Reducing Data-Plane State: Solution
For hundreds of participants’ policies, few millions  < 35K
flow rules

## Slide 31: Reducing Control-Plane Computation
Initial policy compilation time
  Leveraged domain-specific knowledge of policies
  Hundreds of participants requires < 15 minutes
Policy recompilation time
  Leveraged bursty nature of BGP updates
  Most recompilation after a BGP update < 100 ms

## Slide 32: SDX Testbed
Mininet-based Testbeds
  Uses Transit Portal
  Emulates edge routers
Check out our demo
  Application specific peering
  Inbound traffic engineering
Github repo: https://github.com/sdn-ixp/sdx/

## Slide 33: Summary
SDN-based exchange (SDX) is promising for fixing Internet routing
Solved various challenges in building a real deployable SDX
Many open research problems, both for building and using SDX