## Slide 1
Declarative Network Path Queries
Srinivas Narayana
May 13, 2016
Advisor: Prof. Jennifer Rexford
Notes: 1
How to simplify network management using a declarative system

## Slide 2: Management = Measure + Control
Network Controller
Measure
Control
Software-Defined Networking (SDN)
Notes: Knowing what’s going on is harder than knowing what to do about it

## Slide 3: Enabling Easier Measurement Matters
Networks are asked to do a lot!
  Partition-aggregate applications
  Growth in traffic demands
  Stringent performance requirements
  Avoid expensive outages
Difficult to know where things go wrong!
  Humans are slow in troubleshooting
  Human time is expensive
Can we build programmatic tools to help?

## Slide 4: Example: Where’s the Packet Loss?
A
B
Suspect: Faulty network device(s) along the way.
1000 pkts
850 pkts 

## Slide 5: Example: Where’s the Packet Loss?
A
B
Idea: “Follow” the path of packets through the network.
Switch ACL counters
1000 pkts
850 pkts 
ip.src==a & ip.dst==b
ip.src==a &
ip.dst==b’
ip.src==a & ip.dst==b  count
ip.dst==b  fwd port 2
Packet rewrite
NetFlow
Sampling Inaccuracy
Notes: HSA/VeriFlow  can we talk about that?

## Slide 6: Example: Where’s the Packet Loss?
Complex & Inaccurate Join
with multiple datasets: traffic, forwarding, topology
High Overhead
of collecting (unnecessary) data to answer a given question

## Slide 7: Example: Where’s the Packet Loss?
Complex & Inaccurate Join
with multiple datasets: traffic, forwarding, topology
High Overhead
of collecting (unnecessary) data to answer a given question

## Slide 8: Pattern: Combining Traffic & Forwarding
Traffic matrix
Uneven load balancing
DDoS source identification
Port-level traffic matrix
Congested link diagnosis
Slice isolation
Loop detection
Middlebox traversal order
Incorrect NAT rewrite
Firewall evasion
...
Resource management
Policy enforcement
Problem diagnosis
Sources: Feldman et al 2001, Patel et al 2013, Savage et al 2000, Varghese and Estan 2004, Duffield and Grossglauser 2001, Kazemian et al 2012, Fayazbakhsh et al 2014, Handigol et al 2014, Zhu et al 2015, and conversations with network operators at Microsoft and Amazon
Notes: Yet, challenging:
  Accuracy: Hard to infer trajectories in data plane
  Efficiency: bandwidth, packet bits, rules
  Composition: measurements with forwarding

## Slide 9: Approach
Declarative Query Specification
Query-Driven Measurement
Path Query System
Independent of Forwarding
Independent of Other Measurements
Independent of Hardware Details
Accurate Answers
Pay Exactly For What You Query
Commodity (“Match-Action”) Hardware
Path Query Language
Query Run-Time System
Notes: Mention the term match-action here?

## Slide 10: Approach
1. Path Query Language
2. Query Run-Time System
SDN controller
Payloads
Statistics
Query Expressions
Statistics
Forwarding
3. Optimizations

## Slide 11: Approach
1. Path Query Language
2. Query Run-Time System
3. Optimizations
Expressive measurement specification
Accurate data plane measurement
Efficient measurement

## Slide 12: Contributions
Regular-expression-based language for traffic monitoring
  With SQL-like aggregation and capture locations
Run-Time: Deterministic finite state automata on packets using match-action switch rules
  Collect exactly those packets that satisfy queries
Compiler optimizations: to speed up or completely remove expensive overlapping actions on packets
Result: Debug networks with practical overheads

## Slide 13
How to design general measurement primitives
… that are efficiently implemented
in the network?

## Slide 14: Measurement Use Cases
Traffic matrix
Uneven load balancing
DDoS source identification
Port-level traffic matrix
Congested link diagnosis
Slice isolation
Loop detection
Middlebox traversal order
Incorrect NAT rewrite
Firewall evasion
...
What are the common patterns?
Sources: Feldman et al 2001, Patel et al 2013, Savage et al 2000, Varghese and Estan 2004, Duffield and Grossglauser 2001, Kazemian et al 2012, Fayazbakhsh et al 2014, Handigol et al 2014, Zhu et al 2015, and conversations with network operators at Microsoft and Amazon
Notes: “We looked at a wide variety of measurement use cases, and we came up with the following abstractions”
Yet, challenging:
  Accuracy: Hard to infer trajectories in data plane
  Efficiency: bandwidth, packet bits, rules
  Composition: measurements with forwarding

## Slide 15: (I) Path Query Language
Test predicates on packets at single locations:
  srcip=10.0.0.1
  port=3 & dstip=10.0.1.10
Combine tests with regular expression operators!
  sw=1 ^ sw=4
  srcip=A ^ true* ^ sw=3
  ingress() ^ ~(sw=firewall)* ^ egress()
ingress
egress
ingress
ingress
egress
egress
Notes: -- Remove before or after

## Slide 16: (I) Path Query Language
Aggregate results with SQL-like grouping operators
  in_group(ingress(), [sw])
  ^ true*
  ^ out_group(egress(), [sw])
Return packets, counters, or samples (NetFlow/sFlow)
ingress() switch | #pkts
S1 | 1000
S2 | 500
S5 | 700
... | ...
(ingress(), egress()) switch pairs | #pkts
(S1, S2) | 800
(S1, S5) | 200
(S2, S5) | 300
... | ...

## Slide 17: (I) Path Query Language
Capture upstream, downstream or midstream
Match predicates at switch ingress, egress or both
  in_atom(dstip=128.1.2.3)
  in_out_atom(dstip=128.1.2.3, dstip=10.1.2.3)
Packet flow on query path
Upstream
Downstream
Midstream

## Slide 18: (I) Evaluation: Query Examples
Sources: Feldman et al 2001, Patel et al 2013, Savage et al 2000, Varghese and Estan 2004, Duffield and Grossglauser 2001, Kazemian et al 2012, Fayazbakhsh et al 2014, Handigol et al 2014, Zhu et al 2015, and conversations with network operators at Microsoft and Amazon

## Slide 19: (I) Language: Related Work
Primitive | Description | Prior Work | Our Extensions
Atomic Predicates | Boolean tests on located packets | [Foster11] [Monsanto13] | Switch input and output differentiation
Packet Trajectories | Regular expressions on atomic predicates | [Tarjan79], [Handigol14] | Additional regex operators (&, ~)
Result Aggregation | Group results by location or header fields | SQL groupby, [Foster11] | Group anywhere along a path
Capture Location | Get packets before or after queried path | -- | N/A
Capture Result | Actions on packets satisfying queries | [Monsanto13] | Sampling (sFlow); path-based forwarding
Notes: Fast algorithms for solving path problems. Robert Tarjan. Stanford technical report, 1979. http://infolab.stanford.edu/pub/cstr/reports/cs/tr/79/734/CS-TR-79-734.pdf

## Slide 20
How do we implement
path queries efficiently?
In general, switches don’t know prior or future packet paths.
Notes: Yet, challenging:
  Accuracy: Hard to infer trajectories in data plane
  Efficiency: bandwidth, packet bits, rules
  Composition: measurements with forwarding

## Slide 21: Match-Action Packet Processing
21
match1  action1
match2  action2
...
(Ternary) Bit Pattern, e.g.,
srcip=A
Forward/Drop/Modify
dstipB;
fwd(2)
Multiple but limited # stages (e.g., 16)
Limited # rules per stage (e.g., 2K)

## Slide 22: How to observe pkt paths downstream?
Analyze packet paths in the data plane itself
  Write path information into packets!
Pros: accurate path information 
Cons: too much per-packet information 
Cons: can’t match regular expressions on switches
[{sw: S1
port: 1
srcmac: ...
srcip: ...
...}]
[{sw: S1, ...},
{sw: S2
port: 3
srcmac: ...
...}]
[{sw: S1, ...},
{sw: S2, ...},
{sw: S3
port: 2
...}]

## Slide 23: Reducing Path Information on Packets
Observation 1: Queries already tell us what’s needed!
  Only record path state needed by queries
Observation 2: Queries are regular expressions
  Regular expressions  Finite automaton (DFA)
  Distinguish only paths corresponding to DFA states
Notes: Running a distributed DFA on the network

## Slide 24: Reducing Path Information on Packets
Record only DFA state on packets (1-2 bytes)
Use existing “tag” fields! (e.g., VLAN)

## Slide 25: (II) Query Run-Time System
(sw=1 & srcip=A) ^ (sw=4 & dstip=B)
Q0
Q1
sw=1 & srcip=A
sw=4 & dstip=B
Q2
Switch 1:
state=Q0 & srcip=A  state=Q1
Switch 4:
state=Q1 & dstip=B  state=Q2
AND count!
Notes: At the end, ”in other words, if you only collect packets accepted by queries, you pay for what you query”
Don’t say ”AND” for concatenation!!

## Slide 26: (II) Query Run-Time System
Each packet carries its own DFA state
Query DFA transitions distributed to switches
  … as match-action rules!
Packet satisfies query iff it reaches accepting states
  “Pay for what you query”
Notes: Nuance: cost in the data plane itself… refer to paper?
Packet collection is only one measure of cost. “in the paper we also look at the number of forwarding rules”

## Slide 27: (II) You Pay For What You Query

## Slide 28: (II) Run-Time: Deterministic Transitions
p1: sw=S1
p2: dstip=10.0.0.2
Q0
Q1
Q2
dstip 10.0.0.2
dstip 10.0.0.2
sw=S1
Switch S1
accept p2
accept p1

## Slide 29: (II) Run-Time: Deterministic Transitions
p1: sw=S1
p2: dstip=10.0.0.2
Trouble: Packet should only be in one automaton state!
Q0
Q1
Q2
dstip 10.0.0.2
dstip 10.0.0.2
sw=S1
Switch S1
accept p2
accept p1

## Slide 30: (II) Run-Time: Deterministic Transitions
p1: sw=S1
p2: dstip=10.0.0.2
Solution: Split predicates into disjoint parts
Q0
Q1
Q3
dstip 10.0.0.2
p1 & ~p2
Switch S1
Q2
Q4
~p1 & ~p2
accept p1 only
accept p2 only
accept p1 and p2
dead
~p1 & p2
p1 & p2

## Slide 31: (II) Run-Time: Composition
All acting on the same data plane packets!
Use policy composition operators and compiler
DFA-Transitioning
Forwarding
DFA-Accepting
>>
+
)
(
Composing software-defined networks. Monsanto et al., 2013
A fast compiler for NetKAT. Smolka et al., 2015
Notes: Why does this composed policy make sense? Explain.

## Slide 32: (II) Run-Time: Composition
DFA-Transitioning
Forwarding
DFA-Accepting
>>
+
)
(
state=Q0 & switch=S1 & srcip=A  stateQ1
state=Q1 & switch=S4 & dstip=A  stateQ2
dstip=A  fwd(1)
dstip=B  fwd(2)
dstip=C  fwd(3)
...
>>
state=Q0 & switch=S1 & srcip=A & dstip=B
 stateQ1, fwd(2)
Openflow 1.0
(for example)
Composing software-defined networks. Monsanto et al., 2013
A fast compiler for NetKAT. Smolka et al., 2015
Notes: Why does this composed policy make sense? Explain.

## Slide 33: (II) Run-Time: Generate Switch Rules
33
match1  action1
match2  action2
...
Bit pattern:
state=Q0 & switch=S1 & srcip=A & dstip=B
Forward/Drop/Modify
stateQ1;
fwd(2)
Result: unified switch rules for forwarding and measurement

## Slide 34: (II) Run-Time: Other details in paper…
Handle groupby aggregation
Testing predicates before and after forwarding
Upstream query compilation
Notes: Maybe add netflow support?

## Slide 35: (II) Run-Time: Related Work

## Slide 36
How well does it work?
Notes: Yet, challenging:
  Accuracy: Hard to infer trajectories in data plane
  Efficiency: bandwidth, packet bits, rules
  Composition: measurements with forwarding

## Slide 37: Evaluation of initial prototype
Prototype on Pyretic + NetKAT + OpenVSwitch
  Publicly available: http://frenetic-lang.org/pyretic/
Queries: traffic matrix, DDoS detection, per-hop packet loss, firewall evasion, slice isolation, congested link
Run all queries together on Stanford backbone
  Compile time: > 2 hours
  Switch rules: (estimated per switch) 1M
  Packet state: 10 bits

## Slide 38: Problem: Cross-Products
DFA-Transitioning
Forwarding
DFA-Accepting
>>
+
)
(
state=Q0 & switch=S1 & srcip=A  stateQ1
state=Q1 & switch=S4 & dstip=A  stateQ2
dstip=A  fwd(1)
dstip=B  fwd(2)
dstip=C  fwd(3)
...
>>
state=Q0 & switch=S1 & srcip=A & dstip=B
 stateQ1, fwd(2)
Notes: Why does this composed policy make sense? Explain.

## Slide 39: Problem: Cross-Products
p1: sw=S1
p2: dstip=10.0.0.2
Q0
Q1
Q2
dstip 10.0.0.2
sw=S1
accept p2
accept p1
Q0
Q1
Q3
p1 & ~p2
Q2
Q4
~p1 & ~p2
accept p1 only
accept p2 only
accept p1 and p2
dead
~p1 & p2
p1 & p2

## Slide 40: Complexity From Overlaps

## Slide 41: Complexity From Overlaps

## Slide 42: (III) Optimizations: Reduce Pkt Overlap
Construct non-overlapping policies
  Use structure of generated Pyretic policies
Remove overlapping actions on packets
  Use pipelined packet processing
Speed up detection of overlapping actions
  Use better data structures & caching
Notes: Emphasize that the highlighted optimizations are among the most non-obvious of the optimizations here. Also, significant gains.

## Slide 43: (III) Optimizations: Summary
Optimization | # Rules? | Time? | # States?
Separate query & forwarding actions into separate stages |  |  | 
Optimize conditional policy compilation |  |  | 
Integrate tagging and capture policies |  |  | 
Pre-partition predicates by flow space |  |  | 
Cache predicate overlap decisions |  |  | 
Decompose query predicates into multiple stages |  |  | 
Detect predicate overlaps with Forwarding Decision Diagrams |  |  | 
Notes: // table of optimizations + intended metrics that should be reduced

## Slide 44: (III) Optimizations: Summary
Optimization | # Rules? | Time? | # States?
Separate query & forwarding actions into separate stages |  |  | 
Optimize conditional policy compilation |  |  | 
Integrate tagging and capture policies |  |  | 
Pre-partition predicates by flow space |  |  | 
Cache predicate overlap decisions |  |  | 
Decompose query predicates into multiple stages |  |  | 
Detect predicate overlaps with Forwarding Decision Diagrams |  |  | 
Notes: // table of optimizations + intended metrics that should be reduced

## Slide 45: (III) Separate Queries from Forwarding
dfa-transition
+
dfa-accept
forwarding
(DFA-Transition >> Forwarding) + DFA-Accept
==
(DFA-Transition + DFA-Accept) >> Forwarding

## Slide 46: (III) Separate Queries from Forwarding
(DFA-Ingress-Transitioning >> Forwarding >> DFA-Egress-Transitioning) +
(DFA-Ingress-Accepting)
+
(DFA-Ingress-Transitioning >> Forwarding >> DFA-Egress-Accepting)
==
(DFA-Ingress-Transitioning + DFA-Ingress-Accepting)
>>
Forwarding
>>
(DFA-Egress-Transitioning + DFA-Egress-Accepting)

## Slide 47: (III) Separating Queries
Set of queries
Another set of queries
Could we run queries in a pipelined fashion?
…

## Slide 48: (III) Separating Queries
  p1: sw=S1; p2: dstip=10.0.0.2; p3: dstip=10.0.0.3
p1
p2
p3

## Slide 49: (III) Separating Queries
  p1: sw=S1; p2: dstip=10.0.0.2; p3: dstip=10.0.0.3
  Problem: Limited # table stages & rules per stage
p1
p2
p3

## Slide 50: (III) Separating Queries
  p1: sw=S1; p2: dstip=10.0.0.2; p3: dstip=10.0.0.3
Idea: Group queries by their “similarity”
  p1 in one stage, p2 and p3 in another
sw=S1  ...
dstip=10.0.0.2...
dstip=10.0.0.3...

## Slide 51: (III) Cost Function for Query Similarity
Input: a set of queries
Output: estimate # rules if queries in same table stage
Concurrent NetCore: From policies to pipelines. Schlesinger et al., 2014
Compiling packet programs to reconfigurable swithces. Jose et al., 2015
Predicate-similarity-aware rule space estimation

## Slide 52: (III) Cost-Aware Query Grouping
Minimize total # stages
Subject to:
  Rule space per stage
  Total number of stages
  One query  one stage
Variables (binary integers)
    Stage j assigned
  Query i assigned to j

## Slide 53: Evaluation
Prototype on Pyretic + NetKAT + OpenVSwitch
  Publicly available: http://frenetic-lang.org/pyretic/
Queries: traffic matrix, DDoS detection, per-hop packet loss, firewall evasion, slice isolation, congested link
Run all queries together on Stanford backbone
  Compile time: > 2 hours  5 seconds
  Switch rules: (estimated) 1M  (actual) ~1K
  Packet state: 10 bits  16 bits
Notes: Rule space estimation for DNF cases.
Stanford forwarding policy has 3840 rules overall – that’s 240 per device on average. Almost all rules match on destination ip address, which almost none of the queries actually match on. This means the best-case reduction applies: ~240 times or two orders of magnitude reduction of rule count going from single-stage to multi-stage tables.
Then there’s at least a factor of 6.6 from the instances that _do_ terminate. Together, that’s 7 * 240 = 1680, or three orders of magnitude reduction in rule space from the unoptimized case.

## Slide 54: Benefit of Optimizations (Stanford)
Cumulative Optimization | Time (s) | # Rules | # State Bits
None | > 7900 | DNF | DNF
Separate query & forwarding actions into separate stages | > 4920 | DNF | DNF
Optimize conditional policy compilation | > 4080 | DNF | DNF
Integrate tagging and capture policies | 2991 | 2596 | 10
Pre-partition predicates by flow space | 56.19 | 1846 | 10
Cache predicate overlap decisions | 35.13 | 1846 | 10
Decompose query predicates into multiple stages | 5.467 | 260 | 16
Notes: Rule space estimation for DNF cases.
Stanford forwarding policy has 3840 rules overall – that’s 240 per device on average. Almost all rules match on destination ip address, which almost none of the queries actually match on. This means the best-case reduction applies: ~240 times or two orders of magnitude reduction of rule count going from single-stage to multi-stage tables.
Then there’s at least a factor of 6.6 from the instances that _do_ terminate. Together, that’s 7 * 240 = 1680, or three orders of magnitude reduction in rule space from the unoptimized case.

## Slide 55: Scalability Trends
Five synthetic ISP (Waxman) topologies at various network sizes
At each network size, run mix of queries from before
  Averaged metrics across queries & topologies

## Slide 56: Evaluation: Scaling
Miller, “Response time in man-computer conversational transactions”
Interactive problem solving (~ 15s)
Notes: Number of data plane rules – mention that you say in the paper
Don’t dwell too much on citation

## Slide 57: II. Rule Count
Switch TCAM capacity: 2K-4K rules

## Slide 58: III. Packet State Bits
VLAN
MPLS

## Slide 59: Conclusions
We need good abstractions to measure networks
  Abstractions must be efficiently implementable
Query-driven measurement: a useful principle
  Improves accuracy; and
  Reduces overheads
Challenge: finding sufficiently general families of questions with efficient solution techniques
Path queries can simplify network management!

## Slide 60: Thanks! 

## Slide 62: Demo: Where’s the Packet Loss?
A
B
1000 pkts
850 pkts 

## Slide 63: Demo: Where’s the Packet Loss?
https://youtu.be/VxOaN9iGPWc

## Slide 64: Discussion: Questions
Control plane versus data plane checking
Switch performance impact (throughput, delay…)
  Table stages
  Memory on the switch
  Memory on the packet
Comparison to existing SDN approaches
System evaluation

## Slide 65: Discussion: Extensions
Multi-packet queries?
  Performance, security, …
  What language abstractions? What hardware?
Post-facto queries
Improving compiler performance

## Slide 66: Approach 1: Join Traffic & Forwarding
Traffic dataset
e.g., NetFlow, SNMP
Forwarding updates
e.g., OF/routing protocol updates
X
Dynamic
Timestamps not aligned!
??
Ambiguity between identical packets downstream
Packet traceback for software-defined networks. Zhang et al., 2015

## Slide 67: Approach 1: Join Traffic & Forwarding
Traffic dataset
e.g., NetFlow, SNMP
Forwarding updates
e.g., OF/routing protocol updates
X
Dynamic
Timestamps not aligned!
??
Ambiguity between identical packets downstream
Trajectory sampling for direct traffic observation. Duffield et al., 2001
Packet rewriting compounds the ambiguity!

## Slide 68: Approach 2: Collect at Every Hop
Using packet histories to troubleshoot networks. Handigol et al., 2014
Hash-based IP traceback. Snoeren et al., 2001
Packet-level telemetry in large data-center networks. Zhu et al., 2015

## Slide 69: Approach 2: Collect at Every Hop
Too expensive to collect up front!
Using packet histories to troubleshoot networks. Handigol et al., 2014
Hash-based IP traceback. Snoeren et al., 2001
Packet-level telemetry in large data-center networks. Zhu et al., 2015

## Slide 70: Approach 2: Collect at Every Hop
Too expensive to collect up front!
Sampling to reduce overhead may miss the packets you care about…
Trajectory sampling for direct traffic observation. Duffield et al., 2001

## Slide 71: Approach 3: Write Path into Packet
sw: S1,
srcip: ___,
dstip: ___,
...
sw: S2,
srcip: ___,
dstip: ___;
sw: S1, ...;
sw: S3, ...;
sw: S2, ...;
sw: S1, ...;
Too much info on packet! :-(
Switches have very accurate info on prior packet path 
IP record route, RFC 791. Postel, 1981
Tracing packet trajectory in data-center networks. Tammana et al., 2015
Match-action HW can’t match regexes :-(

## Slide 72: Reachability Testing for Accepted Pkts
policy p
Static checking for networks, Kazemian et al. NSDI ‘12
??

## Slide 73: Reachability Testing for Accepted Pkts
“Effective” policy after
downstream compilation of query q
Static checking for networks, Kazemian et al. NSDI ‘12
??
state=accepted(q)

## Slide 74: Complexity from Overlaps