## Slide 1: Scalable Real-Time Bandwidth Fairness in Programmable Switches
Robert MacDavid, Xiaoqi Chen, Jennifer Rexford
INFOCOM 2023 May 17th,2023
Notes: Jen‘s feedback on AHAB talk slides. For INFOCOM
I do think the talk errs too much on the side of summarizing the paper, rather than on advertising the paper. Granted, for the Pronto audience, they’ll have already bought into the challenges of PISA data places and the motivation. But, for INFOCOM, you’ll probably want to focus more on motivation and less on being complete.
you have a lot of graphs and results. you may want to — particularly for the infocom talk — have fewer graphs.

## Slide 2: Network Slicing and Bandwidth Fairness
Each slice / user gets a fair share of bandwidth
* For simplicity, all slices and users have equal weight. Trivial to add weighted case.

## Slide 3: Network Slicing and Bandwidth Fairness
If some user or slice is underutilized, fairly re-allocate the surplus
Each slice / user gets a fair share of bandwidth
User 1a, 3a go offline User 2a needs only 20

## Slide 4: AHAB: Scalable hierarchical bandwidth fairness
Goal: Support thousands of slices, millions of users
CPU-based Software switch? High latency
Programmable switch? Hardware constraints
  8-32 hardware queues per port
  Limited arithmetic
  Small memory

## Slide 5: AHAB: Scalable hierarchical bandwidth fairness
Challenge 1: can’t easily calculate the per-user fair rate limit
Solution: guess a limit, closed-loop iterative update
Challenge 2: can’t use per-user memory to track sending rate
Solution: CMS-LPF sketch, approximate per-user rate

## Slide 6: Outline
Problem definition & challenge
Finding bandwidth limit using closed-loop iterative update
Avoiding per-user memory using CMS-LPF sketch
Implementation on Tofino
Evaluation: Fast, Accurate, and Scalable

## Slide 7: Challenge 1: Finding fair per-user rate limit
Sort and plot all user’s bandwidth demand
Apply limit Tn
Total bandwidth used is shaded area f(Tn)
Demand: 20Mbps
Demand: 180Mbps Limited to: 110Mbps
Tn 110Mbps

## Slide 8: Challenge 1: Finding fair per-user rate limit
The ”right” limit means total usage equals capacity:
Cn =f(Tn)
But how do we find Tn? Just guess and refine!
Demand: 20Mbps
Demand: 180Mbps Limited to: 110Mbps
Tn 110Mbps

## Slide 9: Fair rate limit via closed-loop refinement
Adjust T : pick 3 candidates, track 3 hypothetical demands

## Slide 10: Fair rate limit via closed-loop refinement
Plot f(T ) on Y-axis. X-axis is different T limits
We can then map Cn into Tnew , via linear interpolation
Repeat every epoch, until convergence

## Slide 11: Challenge 2: Tracking per-user sending rate
Rate limit T can be enforced via probabilistic drop*: p= (1-T/R) But this requires knowing sending rate R
How to get per-user sending rate, without per-user memory?
Idea: we only care about heavy users… Use sketch!
* Disclaimers:
Only when R >T
This is for UDP. For TCP needs something fancier (see paper)

## Slide 12: Solving scalability challenge: CMS-LPF sketch
Count-Min Sketch: approximate data structure for heavy-hitter flows
Low-Pass Filter: self-decaying counter for exponential moving average
CMS-LPF: approximate per-user sending rate
0 | +1 | 0 | 0 | 2
14 | 0 | +1 | 5 | 0
7 | 0 | 23 | 0 | +1
h1(id) h2(id)
h3(id)
Pkt
Flow id
Pkt
Time, Pkt size
Σ
Average total sending rate
Σ
Σ
Σ
Σ
Σ
Σ
Σ
Σ
Σ
Σ
Σ
Σ
Σ
Σ
Σ
h1(id) h2(id)
h3(id)
T, uid, size
Pkt
min
Estimate
flow size
Estimate per-user sending rate
min

## Slide 13: AHAB’s Hardware implementation on Tofino
First, look up slice id n and its current per-user rate limit Tn ; Also, use CMS-LPF to get estimated per-user sending rate R .
Approximated probabilistic dropping (using match-action rules).
Linear interpolation for new rate limit Tnew ; update using messenger packets.

## Slide 14: Evaluation overview
1. How fast can AHAB converge to the right limit?
✓ 3.1ms, 13x faster than state-of-the-art
2. How fair (accurate)?
✓ Throughput within 4%-6% of ideal fair rate
3. Can AHAB scale?
✓ Millions of users

## Slide 15: Eval 1: Fast convergence
Setup: 1 to 4 flows sharing a slice (fixed 100Mbps capacity)
Compare AHAB with prior state-of-the-art, HCSFQ

## Slide 16: Eval 1: Fast convergence to fairness
AHAB’s iterative update converges in 3.1ms
Instead, HCSFQ needs 42ms to converge (13x)

## Slide 17: Eval 2: Accuracy
Flows with different demands: 10Mbps, 20Mbps, 30Mbps…160Mbps Enforced to within 4%-6% of fair bandwidth limit.

## Slide 18: Eval 3: Scalability
# of Users | CMS-LPF size needed | SRAM utilization
3 millions | 2048x3 (24KB) | 1.56%
6 millions | 4096x3 (48KB) | 2.60%
24 millions (est.) | 16384x3 (768KB) | 8.85%
Simulate CMS-LPF errors for a very large number of users, using local ISP trace (6M users) and CAIDA (7.3M users)
HW Resource | Instr. Words | Hash Unit | TCAM | Stages
Utilization | 28.6% | 37.5% | 5.2% | 12+9
Other hardware resource metrics

## Slide 19: Summary, Q&A
AHAB: scalable bandwidth fairness, with slicing/hierarchy
using closed-loop iterative refinement to find rate limits,
and CMS-LPF sketch for estimating per-user sending rate.
Runs on today’s switches
Converges in milliseconds
Supports millions of users
https://github.com/ Princeton-Cabernet/AHAB